How to remove a Bella final drive shaft oil seal
The original Zündapp Bella final drive oil seal has a metal housing and can be quite stuck. To remove it without removing the drive shaft itself a custom tool works best.
To make one you will need:
- 2 aluminum discs 8x32 mm (e.g. from lasermaster.co.uk): 6 GBP
- 8 steel 3mm rods of 10 cm: 12 GBP
- 1 M6 x 40 bolt: 1 GBP
- 1 hose pipe clamp 36-39 mm: 1.60 GBP
- 1 Elastic band
Total cost: 20.60 GBP
To create the tool follow these steps:
1. First drill a 5mm hole in the middle of one of the discs and tap M6 thread into the hole. Next drill 8 3.5mm holes in the rim of the threaded aluminum disc to a depth of 11 mm
2. Clamp 8 or 9 mm of the rods in a vise and hammer to 90 degrees. Make another 90 degree 60mm further down in the opposite direction. Finally grind down the second bend so it sticks out about 2mm. It’s a bit of work but the result looks as follows:

That’s all you need.
Next is removing the oil seal. First remove as much of the rubber as you can so the seal is ready for removal; this will allow the hooks to be placed. Put the whole aluminum disc on top the shaft. Next, lodge the hooks between shaft and seal and insert them into the holes in the rim of the threaded disc one by one. You can use an elastic band to keep them in place. Next put the hose clamp over the top of the stack and pull the seal out.

Pulling the seal is easy and you’re left with a seal puller for the next job.
This tool should work for any Zündapp engines with a final drive shaft extruding 35 mm with a 32 x 45 x 7 seal.